## Slide 1: Dylan’s Update
26 June 2019

## Slide 2: Vacuum Feedthrough Original Design
Slot design allows for customisation of connectors
Mechanically strong
Great signal isolation and ground coupling
Assembly
External connectors attached with high-temp solder
PCBs inserted, internal connectors attached with high-temp solder
Boards and brass rods fixed in place with low-temp solder
Epoxy applied

## Slide 3: Vacuum Feedthrough “Problems”
Long assembly time, many steps in procedure
Complex design
Prone to mistakes: solder bridges, misalignment, component slipping
  Most impossible to fix
Doesn’t fit in conventional KF adapters
Many potential points of entry for air

## Slide 4: New Feedthrough Design
All components mounted directly on board
  Reduces assembly time and cost
  Fewer opportunities for leaks
  Short trace lengths
Smaller connector, same # of pins
  More signals in same space
  S-S-S as opposed to G-S-G
Two designs on developmental version
  Vias in a row vs vias alternating
Needs modified o-ring to work
  Clipped top section, 3d printed

## Slide 5: PCB Feedthrough Goals
Add as many connectors as physically possible
Achieve higher vacuum/tighter seal
  Spacers, two boards, better o-ring
Keep it as simple as possible
Things still left to do:
Perform leak check
  Ensure that there’s more than a superficial seal
Measure crosstalk
  See if S-S-S config is tenable in full setup